## Slide 1: Homework 2
Kody Davis - 5375

## Slide 2: Register File Module
Each block of code corresponds to a unit in the blueprint
  Load Gates
  Registers
  4-to-1 Mux
  2-to-4 Decoder

## Slide 3: Register File Module
The outputs of the module are the outputs of the two 4-to-1 mux modules
The inputs to the module are:
  clk – clock signal (not pictured, only for registers)
  reset – reset signal (not pictured, only for registers)
  aReg_select – mux select signal for operandA
  bReg_select – mux select signal for operandB
  load_enable – load enable signal
  dest_select – decoder signal
  reg_data – data to be placed in a register

## Slide 4: Testbench
Make assignments on the positive edge of the clock signal
  If the assignments were made in the middle of the clock cycle, the signals “aReg_select” and “bReg_select” would cause the output of the MUXs to change in the middle of the cycle, causing problems if an adder unit was attached.
  The clock signal is blocking (=), while the assignment signals are non-blocking (<=). This means the clock tick happens first (capturing “reg_data” in Register “dest_select”) and then the new assignments happen.
Initially, set everything to 0 and set reset to 1
Then, set reset to 0 and load_enable to 1
The for-loop places values 1-4 in Registers 0-3, respectively. It also sets the MUX signals to output the value of the register that was just given a value (“operandA” and operand”).

## Slide 5: Testbench
Clock tick happens
  reset is set to 0
  load_enable is set to 1
  dest_select stays 0 (data will be put in reg0)
  reg_data is set to 1
  aReg_select and bReg_select are set to 0 so,
  operandA and operandB output 0
Clock tick happens
  Previous “reg_data”(1) is captured in previous register “dest_select” (0)
  “dest_select” is set to new destination register(1)
  “reg_data” is set to new value to be captured at next clock tick
  “aReg_select” and “bReg_select” are set to 0 so,
  “operandA” and “operandB” output 1 (value in reg0)
Clock tick happens
  Previous “reg_data”(2) is captured in previous register “dest_select” (1)
  “dest_select” is set to new destination register(2)
  “reg_data” is set to new value to be captured at next clock tick
  “aReg_select” and “bReg_select” are set to 1 so,
  “operandA” and “operandB” output 2 (value in reg1)
Etc…

## Slide 6: Testbench and Simulation