## Slide 1: Homework 4
Kody Davis - 5375

## Slide 2
MC MM MR DSA SB MA MB MD FS MO
2 2 1 00 00 0 0 0 00 0
CAR  ROM[ 10001 || MODE || X ]
CAR needs to get its new value from Mapping ROM. Since MO = 0 (NOP) and MC = 2, RW(register write) is enabled. Therefore, all other values should be 0 so that the value 0 is written to register 0.
1OF IDI
No asterisk(*), meaning this operation does NOT prevent write to register file.
(101)

## Slide 3
MC MM MR DSA SB MA MB MD FS MO
0 X X 0E XX 1 X 1 XX 5
DA  M[ PC ], PC  PC + 1
Use DA for temp storage since we will be referencing an address later.
DA gets the value located at the memory address PC.
Increment the PC counter. (MO = 5)

## Slide 4
MC MM MR DSA SB MA MB MD FS MO
0 X X 0E 10XXX 0 0 0 02 0
DA  DA + R[ DST ]
Use DA for temp storage since we will be referencing an address later.
DA gets the current value of DA plus the value of the register DST.

## Slide 5
MC MM MR DSA SB MA MB MD FS MO
0 X X 0E 00 0 X 1 XX 0
DA  M[ DA ]
Use DA for temp storage since we will be referencing an address later.
DA gets the value located at the memory address DA.

## Slide 6
MC MM MR DSA SB MA MB MD FS MO
2 0 1 0F 0E 3 X 1 XX 0
DD  M[ DA ], CAR  1EX(ROM)
Use DD for temp storage since we will be executing the rest of the instruction before writing back to a register.
DD gets the value located at the memory address DA.
CAR changes to the proper execution(EX) state for the current operation. This is accomplished by loading the appropriate value from the Mapping ROM.
5 ticks

## Slide 7
MC MM MR DSA SB MA MB MD FS MO
2 2 2 00 00 0 0 0 00 0
CAR  ROM[ 10010 || MODE || 0 ]
CAR needs to get its new value from Mapping ROM. Since MO = 0 (NOP) and MC = 2, RW(register write) is enabled. Therefore, all other values should be 0 so that the value 0 is written to register 0.
2OF IDI (S = 0)
No asterisk(*), meaning this operation does NOT prevent write to register file.
(101)

## Slide 8
MC MM MR DSA SB MA MB MD FS MO
0 X X 0C XX 1 X 1 XX 5
SA  M[ PC ], PC  PC + 1
Use SA for temp storage since we will be referencing an address later.
SA gets the value located at the memory address PC.
Increment the PC counter. (MO = 5)

## Slide 9
MC MM MR DSA SB MA MB MD FS MO
0 X X 0C 11XXX 0 0 0 02 0
SA  SA + R[ SRC ]
Use SA for temp storage since we will be referencing an address later.
SA gets the current value of SA plus the value of the register SRC.

## Slide 10
MC MM MR DSA SB MA MB MD FS MO
0 X X 0C 00 0 X 1 XX 0
SA  M[ SA ]
Use SA for temp storage since we will be referencing an address later.
SA gets the value located at the memory address SA.

## Slide 11
MC MM MR DSA SB MA MB MD FS MO
0 X X 0D 0C 3 X 1 XX 0
SD  M[ SA ]
Use SD for temp storage since we will be executing the rest of the instruction before writing back to a register.
SD gets the value located at the memory address SA.

## Slide 12
MC MM MR DSA SB MA MB MD FS MO
2 0 2 0F 10XXX 3 0 0 00 0
DD  R[ DST ], CAR  1/2EX(ROM)
Use DD for temp storage since we will be executing the rest of the instruction before writing back to a register.
DD gets the value located at the register DST.
CAR changes to the proper execution(EX) state for the current operation. This is accomplished by loading the appropriate value from the Mapping ROM.
6 ticks

## Slide 13
MC MM MR DSA SB MA MB MD FS MO
2 2 2 00 00 0 0 0 00 0
CAR  ROM[ 10010 || MODE || 1 ]
CAR needs to get its new value from Mapping ROM. Since MO = 0 (NOP) and MC = 2, RW(register write) is enabled. Therefore, all other values should be 0 so that the value 0 is written to register 0.
2OF IDI (S = 1)
No asterisk(*), meaning this operation does NOT prevent write to register file.
(101)

## Slide 14
MC MM MR DSA SB MA MB MD FS MO
0 X X 0E XX 1 X 1 XX 5
DA  M[ PC ], PC  PC + 1
Use DA for temp storage since we will be referencing an address later.
DA gets the value located at the memory address PC.
Increment the PC counter. (MO = 5)

## Slide 15
MC MM MR DSA SB MA MB MD FS MO
0 X X 0E 10XXX 0 0 0 02 0
DA  DA + R[ DST ]
Use DA for temp storage since we will be referencing an address later.
DA gets the current value of DA plus the value of the register DST.

## Slide 16
MC MM MR DSA SB MA MB MD FS MO
0 X X 0E 00 0 X 1 XX 0
DA  M[ DA ]
Use DA for temp storage since we will be referencing an address later.
DA gets the value located at the memory address DA.

## Slide 17
MC MM MR DSA SB MA MB MD FS MO
0 X X 0F 0E 3 X 1 XX 0
DD  M[ DA ]
Use DD for temp storage since we will be executing the rest of the instruction before writing back to a register.
DD gets the value located at the memory address DA.

## Slide 18
MC MM MR DSA SB MA MB MD FS MO
2 0 2 0D 11XXX 3 X 0 00 0
SD  R[ SRC ], CAR  1/2EX(ROM)
Use SD for temp storage since we will be executing the rest of the instruction before writing back to a register.
SD gets the value located at the register SRC.
CAR changes to the proper execution(EX) state for the current operation. This is accomplished by loading the appropriate value from the Mapping ROM.
6 ticks

## Slide 19
MC MM MR DSA SB MA MB MD FS MO
2 2 3 00 00 0 0 0 00 0
CAR  ROM[ 10011 || MODE || X ]
CAR needs to get its new value from Mapping ROM. Since MO = 0 (NOP) and MC = 2, RW(register write) is enabled. Therefore, all other values should be 0 so that the value 0 is written to register 0.
BAF IDI
No asterisk(*), meaning this operation does NOT prevent write to register file.
(101)

## Slide 20
MC MM MR DSA SB MA MB MD FS MO
0 X X 0E XX 1 X 1 XX 5
DA  M[ PC ], PC  PC + 1
Use DA for temp storage since we will be referencing an address later.
DA gets the value located at the memory address PC.
Increment the PC counter. (MO = 5)

## Slide 21
MC MM MR DSA SB MA MB MD FS MO
0 X X 0E 10XXX 0 0 0 02 0
DA  DA + R[ DST ]
Use DA for temp storage since we will be referencing an address later.
DA gets the current value of DA plus the value of the register DST.

## Slide 22
MC MM MR DSA SB MA MB MD FS MO
0 X X 0E 00 0 X 1 XX 0
DA  M[ DA ]
Use DA for temp storage since we will be referencing an address later.
DA gets the value located at the memory address DA.

## Slide 23
MC MM MR DSA SB MA MB MD FS MO
2 0 3 0E XX 0 X 1 XX 0
DA  M[ DA ], CAR  BEX(ROM)
Use DA for temp storage since we will be executing the rest of the instruction.
DA gets the value located at the memory address DA.
CAR changes to the proper execution(EX) state for the current operation. This is accomplished by loading the appropriate value from the Mapping ROM.
5 ticks